Cost Details:    Shivgad Tanda, Taluka: Paithan Dist: Aurangabad

| Sr. No. | Budget Head | Volume (cum) / Unit (no) | Rate (Rs) | Total Cost (Rs) | Local Contribution (15% of total cost except sr. no. E) | Total Grant Required (Rs) | Total Grant Required (US$) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| (1) | (2) | (3) | (4) | (5) | (6) | (7) | (8) |
| A] | Digging of new well of 6m diameter |  |  |  |  |  |  |
|  | Upto 3 meter | 3 | 2500.00 | 7500.00 |  |  |  |
|  | 3 to 6 meter | 3 | 4500.00 | 13500.00 |  |  |  |
|  | 6 to 12meter | 6 | 8000 | 48000.00 |  |  |  |
|  | RRC Ring construction | 4 | 6000 | 24000.00 |  |  |  |
|  | Sub total A] |  |  | 93000.00 | 13950.00 | 79050.00 | 1757 |
| B] | Digging of trench for Pipeline 345 M (0.45 m wide and 0.75m deep) | 345 | 12 | 4140.00 |  |  |  |
|  | Cost of pipes, HDP 2.5’’ | 345 | 47 | 16215.00 |  |  |  |
|  | Assembling Material and fitting charges |  |  | 3500.00 |  |  |  |
|  | Air valve, non return valve etc |  |  | 2500.00 |  |  |  |
|  | Excavation of distribution pipe line trench | 225 | 100 | 22500.00 |  |  |  |
|  | Stand post 4 | 4 | 1000 | 4000.00 |  |  |  |
| Sub total B] |  |  | 52855.00 | 7930.00 | 44925.00 | 998 |
| C] | 2 HP submersible pumpset and accessories |  |  | 15000.00 |  |  |  |
|  | MSEB Connection charges |  |  | 35000.00 |  |  |  |
| Sub total C] |  |  | 50000.00 | 7500.00 | 42500.00 | 944 |
| D] | Construction of water storage tank of 15,000 liter capacity @ 4.5/lit |  |  | 67500.00 | 10125.00 | 57375.00 | 1275 |
|  | Sub total D] |  |  | 67500.00 | 10125.00 | 57375.00 | 1275 |
| Total [A+B+C+D] |  |  | 263355.00 | 39505.00 | 223850.00 | 4974 |
| E] Management cost (20% of the total) |  |  | 52670.00 | 0.00 | 52670.00 | 1170 |
| Grand Total |  |  | 316025.00 | 39505.00 | 276520.00 | 6145 |