Cost Details:    Kombadwadi, Taluka: Ambad,  Dist: Jalna

| Sr. No. | Budget Head | Length (m) | Volume (cum) / Unit (no) | Rate (Rs) | Total Cost (Rs) | Local Contribution (15% of total cost except sr. no. D) | Total Grant Required (Rs) | Total Grant Required (US$) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| (1) | (2) | (3) | (4) | (5) | (6) | (7) | (8) | (9) |
| A] | Digging of trench for Pipeline (0.75m deep and 0.45 m width) | 244 |  | 14 | 3416 |  |  |  |
|  | Cost of pipes, 2.5” PVC Rising main | 330 |  | 54 | 17820 |  |  |  |
|  | Cost of pipes, 3” PVC Distribution system | 240 |  | 100 | 24000 |  |  |  |
|  | Pipe fitting material and fitting charges |  |  |  | 3500 |  |  |  |
|  | 1 Non return valve and 2 air valve |  |  |  | 4000 |  |  |  |
|  | Stand post |  | 4 | 1000 | 4000 |  |  |  |
| Sub total A] |  |  | 1000 | 56736 | 8510 | 48226 | 1072 |
| B] | 5 HP Mono block electric pump with accessories |  |  |  | 15000 |  |  |  |
|  | MSEB electricity charges and deposit |  |  |  | 25000 |  |  |  |
| Sub total B] |  |  |  | 40000 | 6000 | 34000 | 756 |
| C] | Construction of Water storage tank of 10000 @ 4.5 per litre capacity |  |  | 4.5 per lit. | 45000 | 6750 | 38250 | 850 |
| Sub total C] |  |  |  | 45000 | 6750 | 38250 | 850 |
| Total [A+B+C] |  |  |  | 141736 | 21260 | 120476 | 2678 |
| D] Management cost (20% of the total) |  |  |  | 28347 | - | 28347 | 630 |
| Grand Total |  |  |  | 170083 | 21260 | 148823 | 3308 |