Valhewadi   - Drinking Water Project

Summary

| S.No | Budget Head | Volume (cum)/ Unit no. | Rate (Rs) | Total Cost (Rs) | Local Contribution (Rs) | Total Grant Required (Rs) | Total Grant Required (USD) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| 1 | Construction of New R.C.C, G.S.R. | As per Annexure - I |  | 1,57,820.00 | 31,564.00 | 1,26,256.00 | 2806 |
| 2 | L.L.& Jointing Distribution system. With P.V.C. Pipe. | As per Annexure - II |  | 2,38,103.00 | 47,621.00 | 1,90,482.00 | 4233 |
| 3 | Providing stand by- 3 BHP Submersible accessories & repairs to Pump house Etc. | As per Annexure - III |  | 30,000.00 | 6,000.00 | 24,000.00 | 533 |
| 4 | Construction of R.C.C, Two Tap Stand Posts | As per Annexure - IV |  | 30,240.00 | 6,048.00 | 24,192.00 | 538 |
| 5 | Training to Beneficiaries | Lump sump |  | 10,000.00 | Nil | 10,000.00 | 222 |
| 6 | Provosion for drinking water | Lump sump |  | 10,000.00 | 2,000.00 | 8,000.00 | 178 |
| 7 | Contengencies | 7% |  | 21,928.00 | 4,386.00 | 17,542.00 | 390 |
| 8 | Plan & Estimates Preparation Charges | Lump sump |  | 2,000.00 | 400.00 | 1,600.00 | 35 |
|  | Total |  |  | 5,00,091.00 | 90,019.00 | 4,02,072.00 | 8935 |
| 9 | Management Cost @ 20% |  |  | 1,00,018.00 | Nil | 1,00,018.00 | 2223 |
|  | Grand Total |  |  | 6,00,109.00 | 98,019.00 | 5,02,090.00 | 11,158 |

Per person cost: USD 21.42

Annexure - I

Valhewadi Rural Water Supply Scheme.

Village :- Valhewadi of Group Grampanchayat- Ghotewadi,

Tal :- Sinnar. Dist :Nashik

Sub Estimate No. 1. R.C.C. G.S.R. Cap. 20,000 Litter

ABSTRACT

| QTY | I.N | Description of Item | Rate | Per | Amount |
| --- | --- | --- | --- | --- | --- |
| 6.56 | 1 | Excavation for foundation in soft strata | 125.00 | cum | 820 |
| 4.53 | 2 | Providing and laying P.C.C. 1:2:4 | 2576.00 | cum | 11669.28 |
|  |  | Providing and constructing U.C.R. Masonry in C.M. 1:6 |  |  |  |
| 3.69 | 3 | A) Below G.L. | 1020.00 | cum | 3763.80 |
| 7.38 | 3 | B) In Super Stretcher | 1048.00 | cum | 7734.24 |
| 13.99 | 4 | Providing Pointing in C.M 1:3 | 34.00 | cum | 475.66 |
| 9.94 | 5 | Filling in plinth with murum. | 33.00 | cum | 328.02 |
| 0.92 | 6 | Providing and fixing in position steel bar reinforcement | 43571.10 | M.T. | 40090.01 |
| 8.77 | 7 | Providing R.C.C. M-200 grade | 4577.00 | cum | 40140.29 |
| 2.77 | 8 | Providing R.C.C.M-150 grade | 3025.00 | cum | 8379.25 |
| 40.00 | 9 | Providing cement plaster 12mm thick in C.M. 1:3 | 125.00 | Sqm | 5000.00 |
| 12.00 | 10 | Providing 80mm dia G.I. pipes. | 433.00 | cum | 5196.00 |
| job | 11 | Providing G.I. specials | Lump Sum | job | 3000.00 |
| 12.00 | 12 | L.L.J. 80mm dia G.I. pipes. | 37.00 | Rmt | 444.50 |
| 2.00 | 13 | A) Providing 80mm dia sluice valves | 3390.00 | No. | 6780.00 |
| 1.00 |  | B) Providing 50mm dia sluice valves | 1916.00 | No. | 1916.00 |
|  | 14 | L.L.J. sluice valves |  |  |  |
| 2.00 |  | A) 80mm dia | 563.00 | No. | 1126.00 |
| 1.00 |  | B) 50mm dia | 230.00 | No. | 230.00 |
| 3.00 | 15 | Providing and constructing valve chambers | 3872.00 | No. | 11616.00 |
| 1.00 | 16 | Providing and fixing C.I.M.H.F.C. | 1320.00 | No. | 1320.00 |
| 1.00 | 17 | Providing and fixing C.I. cowl type Ventilators | 1100.00 | No. | 1100.00 |
|  | 18 | Providing and fixing Ladder |  |  |  |
| 4.50 |  | A) M.S. ladder | 825.00 | Rmt. | 3712.50 |
| 2.30 |  | B) G.I. pipe ladder | 440.00 | Rmt. | 1012.00 |
| 57.86 | 19 | Providing and applying cement paint ect. | 25.30 | Sqm | 1463.86 |
| Job. | 20 | Panting name of the scheme etc. | Lump Sum | Job | 500.00 |
|  |  | Total:- |  |  | 1,57,818.32 |
|  |  | Say Rs:- |  |  | 1,57,820.00 |

Annexure - II

Valhewadi  Rural Water Supply Scheme.

Village :- Valhewadi of Group Grampanchayat- Ghotewadi,

Tal :- Sinnar. Dist :Nashik

Estimate. for Distribution System

| QTY | Description of Item | Rate | unit | Amount Rs. Ps |
| --- | --- | --- | --- | --- |
| A) | MATERIALS. Item no.1-Providing PVC pipes 4kg/cm2 –etc. |  |  |  |
| 480m | i) 90mm dia | 70.00 | M | 33,600.00 |
| 522m | ii) 75mm dia | 50.00 | M | 26,100.00 |
| 706m | iii) 63mm dia | 35.00 | M | 24710.00 |
|  | Item No.2 Providing G.I. pipes Medium Class |  |  |  |
| 12m | i) 80mm dia | 480.00 | M | 5,760.00 |
| 12m | ii)65mm dia | 365.00 | M | 4,380.00 |
| 12m | iii) 50mm dia | 295.00 | M | 3,540.00 |
|  | Item No.3 Providing S.V.PN-I. |  |  |  |
| 1No | i) 80mm dia | 3000.00 | No | 3,000.00 |
| 1No | ii)65 mm dia | 2500.00 | No | 2,500.00 |
| 1No | iii)50mm dia | 2000.00 | No | 2,000.00 |
| Job | Item No.4 Providing PVC & G.I. specials | Lump Sum | Job | 5,000.00 |
| Total.A. :- | 1,10,590.00 |
| B) | Labour Charges. |  |  |  |
| 542.00 | 1)Excavation in Soft Strata & S.M. | 65.00 | cum | 35,230.00 |
| 350.00 | 2) Excavation in H.M.& boulders | 75.00 | cum | 26,250.00 |
| 110.00 | 3)Excavation in Soft Rock | 200.00 | cum | 22,000.00 |
| 140.00 | 4) Providing the murum (soft rock) bedding | 27.00 | cum | 3,780.00 |
| 780.00 | 5)Refilling the pipe Trenches | 25.00 | cum | 19,500.00 |
|  | 6) L.L. & Jointing PVC pipes |  |  |  |
| 480.00 | a) 90 mm dia | 8.70 | M | 4,176.00 |
| 522.00 | b) 75 mm dia | 7.30 | M | 3,810.00 |
| 426.00 | c) 63 mm dia | 5.80 | M | 2,471.00 |
|  | 7) L.L.& Jointing G.I. pipes. |  |  |  |
| 12.00 | a) 80 mm dia | 37.00 | M | 444.00 |
| 12.00 | b) 65 mm dia | 33.00 | M | 396.00 |
| 12.00 | c) 50 mm dia | 23.00 | M | 276.00 |
| Job | 8) Concreting M-150- 1:2:4 for road crossing) gutter & other crossings. ect. | Lump Sum | Job | 5,000.00 |
| 3 Nos. | 9) Providing & fixing C.I Road surface boxes. | 1000.00 | No | 3,000.00 |
|  | 10) Fixing S.V. etc. |  |  |  |
| 1 | a) 80mm | 560.00 | No | 560.00 |
| 1 | b) 65mm | 390.00 | No | 390.00 |
| 1 | c) 50mm | 230.00 | No | 230.00 |
| Total: B.- | 1,27,513.00 |
| Part .A. Total :- | 1,10,590.00 |
| Part .B. Total :- | 1,27,513.00 |
| Total :- | 2,38,103.00 |
| Say Rs. :- | 2,38,103.00 |

Annexure - III

Valhewadi  Rural Water Supply Scheme.

Village :- Valhewadi of Group Grampanchayat- Ghotewadi,

Tal :- Sinnar. Dist :Nashik

Electrical Unit (Stand-By)

| Sr. No | Particulars | Amount |
| --- | --- | --- |
| 1) | Repairs to old submersible 3 BHP Pump, Set. With new S.V. & N.R.V. Submersible cable, earthling & providing armored cable at MSEB. Supply Point. | =Rs. 15,000.00 |
| 2) | Repair to old well ,& switch Room , such as pointing to UCR masonry , fixing required plate & railing to girders fixit in well, repainting of well & switch room etc. | =Rs. 15,000.00 |
| Total Rs. | = 30,000.00 |

Annexure - IV

Valhewadi  Rural Water Supply Scheme.

Village :- Valhewadi of Group Grampanchayat- Ghotewadi,

Tal :- Sinnar. Dist :Nashik

Estimate for R.C.C. Two Tap Stand Post

| Qty | Description of Item | Rate | Unit | Amount |
| --- | --- | --- | --- | --- |
| 5 Nos. | Providing & constructing two tap stand Post as per type design with excavation ,15cm thick boulder filling ,15 cm thick PCC 1:3:L6 bedding 20 mm thick PCC 1:2:4 concrete for platform of 1.75 m dia. with side curb & bucket rest, 80 mm dia. Heavy duty G.I. Central pipe post filled with C.C.1:2:4 5 m long 20 mm dia. G.I. pipe fixed vertically up to 15 mm dia .self closing water tap one brass ferrule. ect to gather with all labour & Materials charges as per drawing ect. Compete. | 6048.00 | No | 30,240.00 |
|  | Total :- | 30,240.00 |